## Slide 1: Simulation Tools for Scaled Vehicle Courses
Chinmay Samak
PhD Candidate, CU-ICAR
csamak@clemson.edu
Tanmay Samak
PhD Candidate, CU-ICAR
tsamak@clemson.edu
AuE-8360 Scaled Autonomous Vehicles

## Slide 2: List of Simulation Tools for Scaled Vehicle Courses
TurtleSim
Official F1TENTH Simulator (Rviz)
Driving Scenario Designer
Gazebo Simulator
F1TENTH Simulator (Gazebo)
CoppeliaSim (formerly V-REP)
F1TENTH Simulator (LGSVL)
Isaac Sim
AutoDRIVE Simulator
DRIVE Sim
CARLA Simulator
LGSVL Simulator
AirSim
AWSim
RaiSim
OpenAI Gym
Ansys Autonomy
CarMaker
CarSim
TORCS
Deepdrive
rFpro
dSPACE AURELION
PreScan
Webots
Cognata
Metamoto
VIRES VTD
GTA V
Project Chrono
Recommended for Courses/Training
Recommended for Research

## Slide 3: TurtleSim
Advantages
  Open source
  Simple & intuitive
  Multi-robot support
Disadvantages
  2D kinematic simulation
  Environments not supported
  Only differential-drive architecture
  No cross-platform support
Simulation Quality | Physics Engine | Graphics Rendering | Vehicle Dynamics Support | Sensor Support | API Support | Developer | Cost | Open Source | Applications
2D | Custom (kinematic simulation) | OpenGL | No | Pose | ROS, ROS 2 | Open Robotics | Free | Yes | Exploration and understanding
Source: Tinker Twins GitHub
Source: ROS Wiki
Source: ROS Core Stacks

## Slide 4: Official F1TENTH Simulator (RViz)
Advantages
  Open source
  Simple & intuitive
  Uses same stack as real vehicle
Disadvantages
  2D simplistic simulation
  No vertical/roll/pitch dynamics
  2D environment representation
  No cross-platform support
  Inaccuracies (e.g., 360° LIDAR simulation - real is 270°)
Simulation Quality | Physics Engine | Graphics Rendering | Vehicle Dynamics Support | Sensor Support | API Support | Developer | Cost | Open Source | Applications
2D | Custom (single track dynamics) | RViz | Single-track dynamics | 2D LIDAR | ROS, ROS 2, Autoware | UPenn | Free | Yes | Exploration, understanding, course, competition
Source: F1TENTH

## Slide 5: MathWorks Driving Scenario Designer
Advantages
  Simple & intuitive
  Multi-agent support
  Comprehensive sensor suite
Disadvantages
  Commercial product
  2D/3D simplistic visualization
  Simplistic trajectory replay
Simulation Quality | Physics Engine | Graphics Rendering | Vehicle Dynamics Support | Sensor Support | API Support | Developer | Cost | Open Source | Applications
2D/3D | N/A | MATLAB App | No | Camera, RADAR, LIDAR, INS, Ultrasonic | MATLAB, Simulink | MathWorks | Paid License | No | Exploration and understanding
Source: MathWorks

## Slide 6: Gazebo Simulator
Advantages
  Open source
  Multi-agent support
  Comprehensive sensor suite
  General robotics simulation
Disadvantages
  Low fidelity dynamics
  Simplistic visualization
  No cross-platform support
Simulation Quality | Physics Engine | Graphics Rendering | Vehicle Dynamics Support | Sensor Support | API Support | Developer | Cost | Open Source | Applications
3D | ODE | Custom | Yes | Pose, Joint States, Camera, LIDAR, IMU, GPS | ROS, ROS 2 | Open Robotics | Free | Yes | Exploration and prototyping
Source: GazeboSim
Source: Tinker Twins GitHub

## Slide 7: F1TENTH Simulator (Gazebo)
Advantages
  Open source
  Multi-agent support
  Uses same stack as real vehicle
  3D simulation environment
Disadvantages
  Low fidelity dynamics
  Simplistic visualization
  No cross-platform support
Source: f1tenth.dev
Simulation Quality | Physics Engine | Graphics Rendering | Vehicle Dynamics Support | Sensor Support | API Support | Developer | Cost | Open Source | Applications
3D | ODE | Gazebo’s Custom | Yes | 2D LIDAR, Pose TF | ROS | UVA | Free | Yes | Exploration, prototyping, course

## Slide 8: CoppeliaSim (formerly V-REP)
Advantages
  3D simulation environment
  Multiple physics engines
  Cross-platform support
  Extended API support
  General robot simulator
Disadvantages
  Moderate compute requirements
  Medium fidelity graphics
Simulation Quality | Physics Engine | Graphics Rendering | Vehicle Dynamics Support | Sensor Support | API Support | Developer | Cost | Open Source | Applications
3D | PhysX, Bullet, Vortex | Custom | Multi-body physics modules can be adapted for vehicle dynamics | 2D/3D LIDAR, Camera, GNSS, IMU, Encoders, State Variables | ROS, ROS 2, Python, C++ MATLAB | Coppelia Robotics | Free (Edu) | No | Exploration and education
Source: Coppelia Robotics

## Slide 9: F1TENTH Simulator (LGSVL)
Advantages
  3D simulation environment
  Photorealistic graphics
  Cross-platform support
Disadvantages
  Inaccurate parameters
  Heavy compute requirements
  Discontinued
Simulation Quality | Physics Engine | Graphics Rendering | Vehicle Dynamics Support | Sensor Support | API Support | Developer | Cost | Open Source | Applications
3D | PhysX | Unity HDRP | Wheel torque model | 2D LIDAR, Camera | ROS | LG | Free/Paid | Yes | Exploration and research
Source: SVLSimulator

## Slide 10: Isaac Sim
Advantages
  3D simulation environment
  Photorealistic graphics
  Realistic physics
  Cross-platform support
  Indoor robot simulator
Disadvantages
  Extreme compute requirements
  Only NVIDIA RTX supported
Simulation Quality | Physics Engine | Graphics Rendering | Vehicle Dynamics Support | Sensor Support | API Support | Developer | Cost | Open Source | Applications
3D | PhysX | Omniverse | Multi-body physics modules can be adapted for vehicle dynamics | 2D/3D LIDAR, Camera, GNSS, IMU, Encoders, State Variables | Python, ROS 2* | NVIDIA | Free | No | Exploration, education and research
Source: Isaac Sim

## Slide 11: AutoDRIVE Simulator
Advantages
  3D simulation environment
  Photorealistic graphics
  Realistic physics
  Cross-platform support
  Extended API support
  On/off road AVs across scales
Disadvantages
  Moderate compute requirements
Simulation Quality | Physics Engine | Graphics Rendering | Vehicle Dynamics Support | Sensor Support | API Support | Developer | Cost | Open Source | Applications
3D | PhysX | Unity HDRP | Full car model for lateral, longitudinal, vertical and RPY dynamics with tire-terrain interaction | 2D/3D LIDAR, Camera, GNSS, IPS, IMU, Encoders Steering Feedback, Throttle Feedback, State Variables | ROS, ROS 2, Python, C++, MATLAB, Simulink, Webapp | CU-ICAR, NTU, SRMIST | Free | Yes | Exploration, education and research
Source: AutoDRIVE Ecosystem

## Slide 12: References
M. Quigley, K. Conley, B. Gerkey, J. Faust, T. Foote, J. Leibs, R. Wheeler, and A. Ng, “ROS: an open-source Robot Operating System,” in ICRA 2009 Workshop on Open Source Software, vol. 3, Jan 2009. [Online]. Available: http://robotics.stanford.edu/~ang/papers/icraoss09-ROS.pdf
S. Macenski, T. Foote, B. Gerkey, C. Lalancette, and W. Woodall, “Robot operating system 2: Design, architecture, and uses in the wild,” Science Robotics, vol. 7, no. 66, p. eabm6074, 2022. [Online]. Available: https://www.science.org/doi/abs/10.1126/scirobotics.abm6074
V. S. Babu and M. Behl, “f1tenth.dev - An Open-source ROS based F1/10 Autonomous Racing Simulator,” 2020 IEEE 16th International Conference on Automation Science and Engineering (CASE), Hong Kong, China, 2020, pp. 1614-1620, doi: 10.1109/CASE48305.2020.9216949
M. O'Kelly, H. Zheng, D. Karthik and R. Mangharam, “F1TENTH: An Open-source Evaluation Environment for Continuous Control and Reinforcement Learning,” Proceedings of Machine Learning Research, H.J. Escalante R. Hadsell (eds.), Proceedings of the NeurIPS 2019 Competition and Demonstration Track, PMLR, vol. 123, pp. 77-89, December 2020. [Online]. Available: https://proceedings.mlr.press/v123/o-kelly20a.html

## Slide 13: References
N. Koenig and A. Howard, “Design and use paradigms for Gazebo, an open-source multi-robot simulator,” 2004 IEEE/RSJ International Conference on Intelligent Robots and Systems (IROS) (IEEE Cat. No.04CH37566), Sendai, Japan, 2004, pp. 2149-2154 vol.3, doi: 10.1109/IROS.2004.1389727
E. Rohmer, S. P. N. Singh and M. Freese, “V-REP: A versatile and scalable robot simulation framework,” 2013 IEEE/RSJ International Conference on Intelligent Robots and Systems, Tokyo, Japan, 2013, pp. 1321-1326, doi: 10.1109/IROS.2013.6696520
G. Rong et al., “LGSVL Simulator: A High Fidelity Simulator for Autonomous Driving,” 2020 IEEE 23rd International Conference on Intelligent Transportation Systems (ITSC), Rhodes, Greece, 2020, pp. 1-6, doi: 10.1109/ITSC45102.2020.9294422
T. Samak, C. Samak, S. Kandhasamy, V. Krovi, and M. Xie, “AutoDRIVE: A Comprehensive, Flexible and Integrated Digital Twin Ecosystem for Autonomous Driving Research & Education,” Robotics, vol. 12, no. 3, p. 77, May 2023, doi: https://doi.org/10.3390/robotics12030077