## Slide 1: Simulation Setup for Scaled Autonomous Vehicles
Chinmay Samak
PhD Candidate, CU-ICAR
csamak@clemson.edu
Tanmay Samak
PhD Candidate, CU-ICAR
tsamak@clemson.edu
AuE-8360 Scaled Autonomous Vehicles

## Slide 2: Official F1TENTH Simulator - Introduction
Advantages
  Open source
  Simple & intuitive
  Uses same stack as real vehicle
Disadvantages
  2D simplistic simulation (RViz)
  No vertical/roll/pitch dynamics
  2D environment representation
  No cross-platform support
  Inaccuracies (e.g., 360° LIDAR simulation - real is 270°)
Simulation Quality | Physics Engine | Graphics Rendering | Vehicle Dynamics Support | Sensor Support | API Support | Developer | Cost | Open Source | Applications
2D | Custom (single track dynamics) | RViz | Single-track dynamics | 2D LIDAR | ROS, ROS 2, Autoware | UPenn | Free | Yes | Exploration, understanding, course, competition
Source: F1TENTH

## Slide 3: Official F1TENTH Simulator - Setup & Exploration

## Slide 4: AutoDRIVE Simulator - Introduction
Advantages
  3D simulation environment
  Photorealistic graphics
  Realistic physics
  Cross-platform support
  Extended API support
  On/off road AVs across scales
Disadvantages
  Moderate compute requirements
  Small development team
Simulation Quality | Physics Engine | Graphics Rendering | Vehicle Dynamics Support | Sensor Support | API Support | Developer | Cost | Open Source | Applications
3D | PhysX | Unity HDRP | Full car model for lateral, longitudinal, vertical and RPY dynamics with tire-terrain interaction | 2D/3D LIDAR, Camera, GNSS, IPS, IMU, Encoders Steering Feedback, Throttle Feedback, State Variables | ROS, ROS 2, Python, C++, MATLAB, Simulink, Webapp | CU-ICAR, NTU, SRMIST | Free | Yes | Exploration, education and research
Source: AutoDRIVE Ecosystem

## Slide 5: AutoDRIVE Simulator - Digital Twin Capabilities
Source: AutoDRIVE Ecosystem
Nigel (Native Scaled Vehicle)
F1TENTH (Scaled Vehicle)
RZR (Off-Road Full Scale Vehicle)
OpenCAV (On-Road Full Scale Vehicle)

## Slide 6: AutoDRIVE Simulator - F1TENTH Simulation
Vehicle dynamics
  Rigid-body dynamics
  Suspension dynamics
  Tire dynamics
  Actuator dynamics

## Slide 7: AutoDRIVE Simulator - F1TENTH Simulation
Sensor physics
  LIDAR
  Throttle & steering sensors*
  Incremental encoders*
  Indoor positioning system*
  Inertial measurement unit*
  Cameras*

## Slide 8: AutoDRIVE Simulator - F1TENTH Simulation

## Slide 9: AutoDRIVE Simulator - F1TENTH Simulation

## Slide 10: AutoDRIVE Simulator - F1TENTH Simulation

## Slide 11: AutoDRIVE Simulator - F1TENTH Simulation

## Slide 12: AutoDRIVE Simulator - F1TENTH Simulation

## Slide 13: AutoDRIVE Simulator - F1TENTH Simulation

## Slide 14: AutoDRIVE Simulator - F1TENTH Simulation

## Slide 15: AutoDRIVE Simulator - F1TENTH Simulation

## Slide 16: AutoDRIVE Simulator - F1TENTH Simulation
Live Demo!

## Slide 17: References
M. Quigley, K. Conley, B. Gerkey, J. Faust, T. Foote, J. Leibs, R. Wheeler, and A. Ng, “ROS: an open-source Robot Operating System,” in ICRA 2009 Workshop on Open Source Software, vol. 3, Jan 2009. [Online]. Available: http://robotics.stanford.edu/~ang/papers/icraoss09-ROS.pdf
S. Macenski, T. Foote, B. Gerkey, C. Lalancette, and W. Woodall, “Robot operating system 2: Design, architecture, and uses in the wild,” Science Robotics, vol. 7, no. 66, p. eabm6074, 2022. [Online]. Available: https://www.science.org/doi/abs/10.1126/scirobotics.abm6074
M. O'Kelly, H. Zheng, D. Karthik and R. Mangharam, “F1TENTH: An Open-source Evaluation Environment for Continuous Control and Reinforcement Learning,” Proceedings of Machine Learning Research, H.J. Escalante R. Hadsell (eds.), Proceedings of the NeurIPS 2019 Competition and Demonstration Track, PMLR, vol. 123, pp. 77-89, December 2020. [Online]. Available: https://proceedings.mlr.press/v123/o-kelly20a.html
T. Samak, C. Samak, S. Kandhasamy, V. Krovi, and M. Xie, “AutoDRIVE: A Comprehensive, Flexible and Integrated Digital Twin Ecosystem for Autonomous Driving Research & Education,” Robotics, vol. 12, no. 3, p. 77, May 2023, doi: https://doi.org/10.3390/robotics12030077