## Slide 1: Capstone Project Proposal
Chinmay Samak
PhD Candidate, CU-ICAR
csamak@clemson.edu
Tanmay Samak
PhD Candidate, CU-ICAR
tsamak@clemson.edu
AuE-8360 Scaled Autonomous Vehicles

## Slide 2: Comparative Analysis of Hardware Platforms
T. Samak, C. Samak, S. Kandhasamy, V. Krovi, and M. Xie, “AutoDRIVE: A Comprehensive, Flexible and Integrated Digital Twin Ecosystem for Autonomous Driving Research & Education,” Robotics, vol. 12, no. 3, p. 77, May 2023, doi: https://doi.org/10.3390/robotics12030077

## Slide 3: Comparative Analysis of Simulation Platforms
W. Ding, C. Xu, M. Arief, H. Lin, B. Li and D. Zhao, “A Survey on Safety-Critical Driving Scenario Generation—A Methodological Perspective,” in IEEE Transactions on Intelligent Transportation Systems, vol. 24, no. 7, pp. 6971-6988, July 2023, doi: 10.1109/TITS.2023.3259322
Opportunity!

## Slide 4: AutoDRIVE Ecosystem
  Ackermann-steer, skid-steer, independent 4WD4WS
  1/14 scale open chassis
  Scaled infrastructure
  Small form factor
  Flexible APIs
  High-fidelity simulation
  Mechatronic testbed
  AD + SC applications
  Affordable cost
  Website
  GitHub
  YouTube
Version | Mobile Base | Battery | Computer(s) | Sensor(s) | Actuator(s) | Developer | Release | Cost
Nigel | Open-Source | 5200 mAh | Jetson Nano or Jetson Orin Nano | RPLIDAR A-1, Pi-Cameras, Intel RealSense D435i, 9-Axis IMU, 6-Axis IPS, Encoders, Microphone, Steering Feedback, Throttle Feedback | DC Motors, Steering Servo(s) | CU-ICAR + NTU + SRMIST | 2021 | $450
Source: https://autodrive-ecosystem.github.io
=

## Slide 5: AutoDRIVE Simulator
Advantages
  3D simulation environment
  Photorealistic graphics
  Realistic physics
  Cross-platform support
  Extended API support
  On/off road AVs across scales
Disadvantages
  Moderate compute requirements
  Small development team
Simulation Quality | Physics Engine | Graphics Rendering | Vehicle Dynamics Support | Sensor Support | API Support | Developer | Cost | Open Source | Applications
3D | PhysX | Unity HDRP | Full car model for lateral, longitudinal, vertical and RPY dynamics with tire-terrain interaction | 2D/3D LIDAR, Camera, GNSS, IPS, IMU, Encoders Steering Feedback, Throttle Feedback, State Variables | ROS, ROS 2, Python, C++, MATLAB, Simulink, Webapp | CU-ICAR, NTU, SRMIST | Free | Yes | Exploration, education and research
Source: AutoDRIVE Ecosystem

## Slide 6: Digital Twin Capabilities of AutoDRIVE Ecosystem
Source: AutoDRIVE Ecosystem
Nigel (Native Scaled Vehicle)
F1TENTH (Scaled Vehicle)
RZR (Off-Road Full Scale Vehicle)
OpenCAV (On-Road Full Scale Vehicle)

## Slide 7: Digital Twin Capabilities of AutoDRIVE Ecosystem
Source: AutoDRIVE Ecosystem

## Slide 8: Digital Twin Capabilities of AutoDRIVE Ecosystem
Source: AutoDRIVE Ecosystem

## Slide 9: Digital Twin Capabilities of AutoDRIVE Ecosystem
Source: AutoDRIVE Ecosystem

## Slide 10: Digital Twin Capabilities of AutoDRIVE Ecosystem
Source: AutoDRIVE Ecosystem

## Slide 11: Planned Project Objectives
ODD focus: on-road autonomous navigation
Platforms:
  Small-scale: Nigel/F1TENTH
  Full-scale: OpenCAV
  Simulation: AutoDRIVE Simulator
  Software-stack: Autoware
True digital twin framework:
  Immersive teleoperation demo
Autoware demo:
  Autonomous navigation (waypoint following)

## Slide 12: References
T. Samak, C. Samak, S. Kandhasamy, V. Krovi, and M. Xie, “AutoDRIVE: A Comprehensive, Flexible and Integrated Digital Twin Ecosystem for Autonomous Driving Research & Education,” Robotics, vol. 12, no. 3, p. 77, May 2023, doi: 10.3390/robotics12030077
W. Ding, C. Xu, M. Arief, H. Lin, B. Li and D. Zhao, “A Survey on Safety-Critical Driving Scenario Generation—A Methodological Perspective,” in IEEE Transactions on Intelligent Transportation Systems, vol. 24, no. 7, pp. 6971-6988, July 2023, doi: 10.1109/TITS.2023.3259322
M. Quigley, K. Conley, B. Gerkey, J. Faust, T. Foote, J. Leibs, R. Wheeler, and A. Ng, “ROS: an open-source Robot Operating System,” in ICRA 2009 Workshop on Open Source Software, vol. 3, Jan 2009. [Online]. Available: http://robotics.stanford.edu/~ang/papers/icraoss09-ROS.pdf
S. Macenski, T. Foote, B. Gerkey, C. Lalancette, and W. Woodall, “Robot operating system 2: Design, architecture, and uses in the wild,” Science Robotics, vol. 7, no. 66, p. eabm6074, 2022. [Online]. Available: https://www.science.org/doi/abs/10.1126/scirobotics.abm6074
Autoware Foundation, “Autoware Project: The world’s leading open-source software project for autonomous driving.” [Online]. Available: https://autoware.org