## Slide 1: Capstone Project Update
Chinmay Samak
PhD Candidate, CU-ICAR
csamak@clemson.edu
Tanmay Samak
PhD Candidate, CU-ICAR
tsamak@clemson.edu
AuE-8360 Scaled Autonomous Vehicles

## Slide 2: Planned Project Objectives
Theme: digital twins + vehicle scale + Autoware
ODD focus: on-road autonomous navigation
Platforms:
  Small-scale: Nigel/F1TENTH
  Full-scale: OpenCAV
  Simulation: AutoDRIVE Simulator
  Software-stack: Autoware
True digital twin framework:
  Immersive teleoperation demo
Autoware demo:
  Autonomous navigation (waypoint following)
Documentation

## Slide 3: Planned Project Objectives
AuE-8360 Capstone Project (Fall 2023) |  |  |  |  |  |  |  | 
Task | 10/18 | 10/25 | 11/01 | 11/08 | 11/15 | 11/22 | 11/29 | 12/06
Announcements |  |  |  |  |  |  |  | 
Project Proposal |  |  |  |  |  |  |  | 
Phase 1 |  |  |  |  |  |  |  | 
Phase 2 |  |  |  |  |  |  |  | 
Phase 3 |  |  |  |  |  |  |  | 
Project Presentation |  |  |  |  |  |  |  | 
Project Report |  |  |  |  |  |  |  | 

## Slide 4: Digital Twin Models in AutoDRIVE Ecosystem
Source: AutoDRIVE Ecosystem
Husky (On/Off-Road Skid-Steer Robot)
Hunter SE (On/Off-Road Ackermann Steered Vehicle)
Nigel (Native Vehicle)
F1TENTH (1/10th Scale Racecar)
RZR (Recreational Off-Highway Vehicle)
OpenCAV (On-Road Commercial Vehicle)
SMALL-SCALE
MID-SCALE
FULL-SCALE

## Slide 5: APIs to connect with AutoDRIVE Ecosystem
Python
C++
ROS
ROS 2
AutoDRIVE
Autoware Integration Complete
[Demo in Progress]

## Slide 6: HMIs to connect with AutoDRIVE Ecosystem
AutoDRIVE
Keyboard+Mouse
Gamepad
Driving Rig
Direct HMI vs. API-Mediated HMI

## Slide 7: AutoDRIVE Ecosystem Update Summary
Computing: Multi-threading & GPU instancing
Profiling: Alienware X15 R2
New Robots: Husky, Hunter SE
Sensors:
  Modularize 2D and 3D LIDARs
  API for 3D LIDAR [Tested with Husky]
Release:
  AutoDRIVE Simulator 0.3.0
  AutoDRIVE Devkit 0.3.0
  LinkedIn Post
Nigel assembly guide and BOM

## Slide 8: Mid-Scale Robot Update Summary
Hunter SE System ID
  Geometric Measurements
  Static measurements
    Mass identification
    CoM identification
  Actuator limits ID [TODO]
Husky System ID
  Geometric Measurements
  Static measurements
    TODO
  Actuator limits ID [in progress]

## Slide 9: F1TENTH Update Summary
Reflash microSD Card with L4T Ubuntu 20.04
  JetPack 5.1.1
  Flashing instructions [1] [2]
Configure hardware/software
  Install VNC for display forwarding
  Install HDMI emulator
  Install and configure Logitech F710 module
  Hokuyo 10LX network configuration
  VESC tuning and configuration
  VESC calibration for odometry (steer/drive)
  Static udev rules for all peripherals

## Slide 10: F1TENTH Update Summary
Reflash microSD Card with L4T Ubuntu 20.04
  JetPack 5.1.1
  Flashing instructions [1] [2]
Configure hardware/software
  Install VNC for display forwarding
  Install HDMI emulator
  Install and configure Logitech F710 module
  Hokuyo 10LX network configuration
  VESC tuning and configuration
  VESC calibration for odometry (steer/drive)
  Static udev rules for all peripherals
Before
After

## Slide 11: F1TENTH Update Summary
Reflash microSD Card with L4T Ubuntu 20.04
  JetPack 5.1.1
  Flashing instructions [1] [2]
Configure hardware/software
  Install VNC for display forwarding
  Install HDMI emulator
  Install and configure Logitech F710 module
  Hokuyo 10LX network configuration
  VESC tuning and configuration
  VESC calibration for odometry (steer/drive)
  Static udev rules for all peripherals
Before
After

## Slide 12: F1TENTH Update Summary
F1TENTH Track Setup
  Small track in lab
  Course track in terrace

## Slide 13: Autoware Update Summary
Compute Platforms
  Alienware X15 R2
  Jetson Xavier NX
Install Autoware Core/Universe
  F1TENTH (local)
  Laptop (local+docker)
  Stable testing with other ROS & ROS 2 distros installed
    F1TENTH (ROS Noetic + ROS 2 Galactic + Autoware Core/Universe)
    Laptop (ROS Noetic + ROS 2 Foxy + ROS 2 Galactic + Autoware Core/Universe)
Autoware Messages
  Create ROS Package (ROS enabled data-processing for Autoware-powered vehicles)

## Slide 14: Autoware on F1TENTH
Install Autoware Core/Universe
  Install ROS 2 Galactic [Install instructions]
  Install ROS Noetic [Install instructions]
  Extreme memory requirements (for build)
  Build failures due to exceeding memory
  Standard errors (ROS DISTROS mismatch)
  Include EOL DISTROS for rosdep update
  Upgrade to 128 GB microSD Card
  64 GB SWAP partition
  Extreme build time (>8 hours)
  Rebuild select packages (faster)
  Caution with ENV variables

## Slide 15: Autoware on F1TENTH
Install Autoware Core/Universe
  Backup src and build of Autoware_WS
  Cloning microSD Card is recommended
Autoware demo
  Test all packages
  SLAM + Record + Replay
  RViz Sim + Real F1TENTH

## Slide 16: References
T. Samak, C. Samak, S. Kandhasamy, V. Krovi, and M. Xie, “AutoDRIVE: A Comprehensive, Flexible and Integrated Digital Twin Ecosystem for Autonomous Driving Research & Education,” Robotics, vol. 12, no. 3, p. 77, May 2023, doi: 10.3390/robotics12030077
W. Ding, C. Xu, M. Arief, H. Lin, B. Li and D. Zhao, “A Survey on Safety-Critical Driving Scenario Generation—A Methodological Perspective,” in IEEE Transactions on Intelligent Transportation Systems, vol. 24, no. 7, pp. 6971-6988, July 2023, doi: 10.1109/TITS.2023.3259322
M. Quigley, K. Conley, B. Gerkey, J. Faust, T. Foote, J. Leibs, R. Wheeler, and A. Ng, “ROS: an open-source Robot Operating System,” in ICRA 2009 Workshop on Open Source Software, vol. 3, Jan 2009. [Online]. Available: http://robotics.stanford.edu/~ang/papers/icraoss09-ROS.pdf
S. Macenski, T. Foote, B. Gerkey, C. Lalancette, and W. Woodall, “Robot operating system 2: Design, architecture, and uses in the wild,” Science Robotics, vol. 7, no. 66, p. eabm6074, 2022. [Online]. Available: https://www.science.org/doi/abs/10.1126/scirobotics.abm6074
Autoware Foundation, “Autoware Project: The world’s leading open-source software project for autonomous driving.” [Online]. Available: https://autoware.org